## Slide 1: Errors in Measurement

## Slide 2: Types of Errors
Basically there are three types of errors on the basis; they may arise from the source.
  Gross Errors
  Systematic Errors
  Random Errors

## Slide 3: Gross Errors
This category of errors includes all the human mistakes while reading, recording and the readings.
Also occur due to incorrect adjustments of instruments
These cannot be treated mathematically
Gross errors can be avoided by using two suitable measures and they are written below:
  A proper care should be taken in reading, recording the data. Also calculation of error should be done accurately.
  By increasing the number of experimenters we can reduce the gross errors. If each experimenter takes different reading at different points, then by taking average of more readings we can reduce the gross errors.

## Slide 4: Systematic Errors
Constant uniform deviation of the operation of an instrument
3 types
    Instrumental Errors
    Environmental Errors
    Observational Errors
  Instrumental Errors
  These errors arise due to 3 main reasons
  i) Due to inherent shortcomings in instrument
  These are due to mechanical structure of instruments Eg:-friction, irregular spring tensions,hysteresis etc

## Slide 5
  It can be avoided by :-
      Selecting a proper instrument & planning proper procedure
      Recognizing the effect of such errors and applying proper correction factors
      Calibrating the instrument carefully against a standard
  ii) Misuse of instruments
  A good instrument if used in abnormal way gives misleading results Eg:- poor initial adjustments, improper zero setting etc
  iii) Loading Effects

## Slide 6: b) Environmental Errors
This type of error arises due to conditions external to instrument.
External condition includes temperature, pressure, humidity, vibrations, dust or it may include external magnetic or electrostatic field.

## Slide 7
Following are the steps that one must follow in order to minimize the environmental errors:
  Try to maintain the surrounding conditions of the laboratory constant by making some arrangements.
  Ensure that there should not be any external magnetic or electrostatic field around the instrument by using magnetic or electrostatic shields
  Using proper correction factors & using the information supplied by the manufacturers of the instrument

## Slide 8: Observational Errors
As the name suggests these types of errors are due to wrong observations.
The wrong observations may be due to parallax while reading a meter, wrong scale selection etc.
Parallax error will be incurred unless the line of vision of the observer is exactly above the pointer
In order to minimize the Parallax error highly accurate meters are required, provided with mirrored scales.

## Slide 9: Parallax error

## Slide 10: Random Errors
After calculating all systematic errors, it is found that there are still some errors in measurement are left. These errors are known as random errors.
Some of the reasons of the appearance of these errors are known but still some reasons are unknown. Hence we cannot fully eliminate these kinds of error
The only way to reduce these errors is by increasing the number of observations & using the statistical methods to obtain the best approximation of the reading

## Slide 11: Statistical analysis
For statistical analysis the same reading is taken number of times. The experimental data is obtained in two forms of tests:-
  i) Multisample test – Repeated measurement of a given quantity is done using different test conditions
  ii) Single sample test – A single measurement is done under identical conditions except for time

## Slide 12
Arithmetic Mean
Deviation from the mean
Average deviation
Standard deviation